## Slide 1
9 July 2014
FAA Data Comm Security Impact Task
Boeing/Airbus

## Slide 2: Introduction, study areas, mitigations

## Slide 3: Boeing/Airbus Tasking
Define data security strategy on ATS data link air-ground segment only
  Why the need, including briefs from the FAA on their assessments
  Which aircraft should be included and technical/cost/other risks
  Timeline for implementation
Define and coordinate Global Data Security solution
  Coordinating findings of Task 1 with standards groups (ICAO: ACP, OPLINK; AEEC: NIS, DLK, DLUF; others as applicable)

## Slide 4: Study Assumptions
Boeing and Airbus used the FAA position as the starting point of analysis
  Threat assessment was not re-done
  Based on their avionics and ATM expertise, some concerns and recommendations are proposed to FAA
Using the provided FAA threat assessments does not mean that Boeing and Airbus endorse them
  Continuing study projects, internal and external, in multiple areas within Boeing and Airbus with wider scope than FAA Data Comm program
  Depending on results, Boeing and Airbus may come up with different conclusions and recommendations

## Slide 5: Boeing/Airbus Concerns
Boeing/Airbus foresee the following risks not having data security mechanisms in place in the long-term
  The threat environment will continue to evolve
  Waiting for an incident creates a long period of exposure
  Cost of wireless attack tools keeps dropping
  Many high security networks have already been penetrated, e.g. US Dept of Defense, banks. No expectation that data link ground networks will remain totally secure (ATSP’s, DCNS, et al)
Concurrently, Boeing/Airbus agree with the significant impacts linked with implementation of data security mechanisms
  Schedule and cost impacts are major, especially to retrofit existing data link equipped fleet
  For FAA, Data Comm program roadmap would need to be redefined; this would jeopardize Data Comm program success

## Slide 6: Near-Term Recommendations (no avionics impact)
Strengthening security of ground networks as much as possible
Ensuring controllers are aware of unsolicited closure messages, may indicate attack
Ensuring flight crew procedures are adequately defined to deal with unsolicited/unexpected messages
Comparison of messages in ground segments
  Matching what is output by ERAM to what is transiting the ground network and uplinked and vice versa
  Routing a copy of all messages sent and received to their originator on the ground segment
Leverage VDL stations to detect spurious signals nearby
Enhanced conformance monitoring for aircraft

## Slide 7: Mid/Long-Term Recommendations (avionics impact)
Establish clear need and definition of requirements that necessitate security solution without compromising existing equipage
Coordinate requirements and solution across regions, defining provisions in international standards
Further investigation of impacts of extensions/modifications to currently-specified solutions
  9880/9705 and 9896
  Secure ACARS (A823)
  Further investigation into and development of simplified 9880 (security shim)

## Slide 8: Other Study Areas
Security solution vs technology
  Need for comm independence may define solution (e.g. TCP or IP-dependent solutions may not be applicable)
  Application vs transport/network level solutions
  Commonality with other existing systems
  Establishing guidelines (e.g. no dialog service impacts)
Secure ACARS impacts, experiences
  Alignment with 9880/9705
  Ramifications of PKI, including certificates management
Establishing timeframe for implementation (convergence)
Refined impact/cost assessments

## Slide 9: Overall concept development

## Slide 10: Prerequisites to Concept
Requires full understanding of entire system, including (but not limited to):
  Establishment of security requirements based on the full-system security architecture concepts (not currently available)
  Technology choices based on the requirements, taking into consideration current and future technologies
  Requirement allocation, including assigning roles and responsibilities
  Determining funding mechanism for concept development, engineering, implementation, and ongoing maintenance and operations.

## Slide 11: Boeing and Airbus Approach
Issues with previous slide:
  Long term task (not something easily done with a short-term study task)
  A continual process with *all* stakeholders
  Technology choices drive concept, and vice versa
Boeing and Airbus identified specific areas that need to be addressed in the continual development of the overall concept
  Impacts on different segments

## Slide 12: Impacts on Aircraft
Key generation, storage, dissemination to relevant applications
  Key sizes and numbers
  Key associations
  Key lifecycles
Key/certificate exchange mechanisms
  Update to comm links necessary?
Application updates to make use of keys
HMI changes to allow interaction with keys when necessary
Potential performance impacts
  Key generation and crypto processing

## Slide 13: Impacts on Aircraft, cont
Other implementation pressures
  Security additions will compete with resources for other added features, fixes
  Additional funding does not necessarily solve this issue
Aircraft performance concerns
  Potential to add additional processing latency
  Could impact end-end transaction times
  New hardware/software requirements
AOC vs ATC
  Secure ACARS in use by some airlines; double security requirements

## Slide 14: Other Impacts
Similar concerns for ANSP, Aircraft operator, ground segment (performance, complexity, scalability, etc)
Public Key Infrastructure overall concept and management
  Deployment, update and obsolescence
  Algorithm choices and usage with international entities
  PKI sourcing
  Additional resource consumption within equipment
  Adapting PKI protocols to operate over non-IP networks
  Roaming aspects
Aircraft Operator, ANSP, Ground Segment Impacts
  Establishing PKI in-house or using PKI services
  Updates to basic operating procedures
  Increased maintenance aspects

## Slide 15: Impacts Major Questions
Assuming international consensus on design is achieved:
  Who pays for all the upgrades, how is that cost distributed?
  Who is responsible for running and maintaining the system?
  Who pays for operation and maintenance?

## Slide 16: Potential technical solutions

## Slide 17: Potential Solution
Different technologies were looked at; part of the difficulty in a final solution is that it must largely be technology agnostic
  Leaves out solutions that are technology dependent, e.g. TLS
An application-level solution similar to the one proposed in ICAO Doc 9880 would be the most likely candidate to satisfy potential security requirements across a broad range of constraints (based on ICAO Doc 9705 Ed 3)
  Authentication-only; can be expanded to provide encryption
Suggestions from the FAA to simplify (relatively) the solution to help with implementation

## Slide 18: Modified Doc 9880 Approach
Created by FAA Tech Center, a modified approach to the current ICAO Doc 9880 has been defined
Simplifies the architecture in a few key areas
  Less complex than ICAO Doc 9705 solution, but still complex nonetheless
  Still needs extensive work to fully specify details
  Not validated
  In-line with ARINC 823
  Once details are specified still need to promulgate through international panels/committees/groups
  Still requires support infrastructure
This solution should be worked on by original parties if possible, to further define specifications and validation

## Slide 19: Boeing Model Impacts
The security function (SSO) needs to be better defined to know the exact hardware needs
B737MAX, B777X, B787, B747-8
  Existing hardware may be sufficient
B737NG, B777, B767/757, B747-400
  Would likely require hardware upgrades
There would be some commonality between models, but each airplane program would need a development program

## Slide 20: Airbus Model Impacts
A320 and A330/A340
  ATN B1 hardware should be capable of hosting data security function
  Pre-FANS, FANS-A/A+ hardware are not capable of hosting data security function
A380 and A350
  Hardware should be capable of hosting data security function
The final solution should be prototyped to ensure hardware compatibility and reduce risk
  Each airplane program would require a development program

## Slide 21: costing

## Slide 22: Costing Considerations
Solution definition:
  Interoperable Air Ground Secure Communications solution: definition costs presumed higher than proprietary solution specific for each aircraft manufacturer, due to interoperability constraints and associated agreements to be reached.
  Specific middleware definition to adapt the existing infrastructures to the interoperable solution
  SECOPS (SECurity Operation Procedures) definition
  Costs mostly for aircraft and equipment manufacturers

## Slide 23: Costing Considerations, cont
Solution development:
  Hardware upgrade: not mandatory depending on the capacities and state of the current hardware platforms
  Higher risk due to hardware technical limitations (fleet age) and certification aspects
  Software development (Security Assurance Level to be defined): mandatory for both interoperable and specific developments – certification aspects.
  Costs mostly for aircraft and equipment manufacturers, and in turn, customers and/or ANSP incentive programs

## Slide 24: Costing Considerations, cont
Solution deployment:
  Hardware deployment on whole fleets depending on the solution development of preceding slide
  Software deployment on whole fleets
  SECOPS integration
  Costs mostly for aircraft manufacturer and airlines, customers and/or ANSP incentive programs
  Still need to define who pays for and maintains the system going forward.

## Slide 25: Boeing/Airbus Costing Assumptions
After analysis of the potential security solution, compared its complexity to that of FANS-2 and FANS-A+C development
Boeing: Estimated per-model cost for security development including Boeing and Supplier
Airbus: Estimated A320 cost for first implementation; projections on other models based on high-level assumptions
Does not include potential additional hardware, if required by certification
Other questions still unanswered that may impact cost (exact location of functionality, assurance level requirements, etc)
Only covers development and potential unit costs
Boeing and Airbus Proprietary cost details delivered to FAA

## Slide 26: roadmap

## Slide 27: Security Roadmap
Assumes that the security requirements are identified and defined
Assumes the security solution will be satisfied by modified Doc 9880
  The solution will be sufficient to mitigate whatever requirements are identified at that time
  The solution is specified well enough for manufacturers to build to an aggressive schedule
Assumes an aggressive, best-case international coordination and collaboration
  All parties agree to the overall approach and ability of solution to satisfy all requirements
  Common procedures are defined and agreed
Does not take into account financial implications of creating and maintaining the infrastructure necessary for security options

## Slide 28: Security Roadmap

## Slide 29: Conclusion

## Slide 30: Conclusion
Based on defined requirements (still TBD at this point), a possible solution to mitigate possible requirements could be the modified Doc 9880 approach
  Further work developing modified ICAO Doc 9880 solution is necessary
Boeing/Airbus agree with the massive impacts linked with implementation of data security mechanisms
  Schedule and cost impacts are major, especially to retrofit existing data link equipped fleet
  For FAA, Data Comm program roadmap would need to be redefined; this would jeopardize Data Comm program success

## Slide 31: Conclusion, cont
A notional, aggressive roadmap shows that approximately 9 years would be required to specify, develop and deploy a security infrastructure from the time of starting such an activity
Both Boeing and Airbus believe that Data Security deployment can only be achieved with a world-wide harmonized position and agree-upon solution
  Between all regions operating and planning to deploy data link
  Based on a consolidated need resulting from a globally convergent threat assessment
  Any differences in implementation will lead to the loss of datalink capability, along with the associated operational and safety benefits

## Slide 32: Backup